024000	Barrel, cylinder	1	G3LS

024207	Barrel, cylinder	1	G80S

023285	Plate, compression, 1/16 in. thick, not Std. Fitting	1	G3LS

023286	Plate, compression, 1/8 in. thick, not Std. fitting	1	G80S

023027	Washer, paper, cylinder base	1	G3LS,G80S

000217	Nut, retaining cylinder to crankcase	4	G3LS,G80S

022711	Head. cylinder with valve guides	1	G3LS

022712	Head, cylinder, with valve guides	1	G80S

010643	Screw, needle adjusting, inlet valve oil feed. (Screws into cylinder head)	1	All singles

011373	Nut, lock, needle adjusting screw	1	All singles

010932	Bolt, securing head to barrel, 3 27/32 in. by 3/8 in. by 20	4	G3LS,G80S

000010	Washer, plain, head securing bolt	4	G3LS,G80S

013793	Gasket, for cylinder head	1	G3LS,G80S

000291	Stud, fixing carburetter, 2 in. by 5/16 in. by 22 by 26	2	All singles

000004	Nut, for carburetter fixing stud	2	All singles

013985	Valve, inlet	1	G3LS

013988	Valve, inlet	1	G80S

013986	Valve, exhaust	1	G3LS

013989	Valve, exhaust	1	G80S

016963	Spring, for valve, wide prong	2	G3LS,G80S

016962	Spring, for valve. narrow prong	2	G3LS,G80S

013990	Collar, for valve spring	2	All singles

023355	Seat, for valve spring	2	All singles

000686	Collet, for valve (each in two pieces)	2	All singles

017019	Guide, for inlet valve	1	All singles

022208	Guide, for exhaust valve	1	G3LS,G80S

011111	Circlip, for exhaust valve guide	1	All singles

018925	Piston, complete	1	G3LS

018927	Piston, complete	1	G80S

018924	Piston, bare	1	G3LS

018926	Piston, bare	1	G80S

018279	Ring, compression, 2 23/32 in. by 1/16 in. (chrome plated)	1	G3LS

010638	Ring, compression, 3 1/4 in. by 1/16 in. (chrome plated)	1	G80S

010634	Ring, compression, 2 23/32 in. by 1/16 in	1	G3LS

010636	Ring, compression, 3 1/4 in. by 1/16 in	1	G80S

010635	Ring, scraper, 2 23/32 in. by I /8 in	1	G3LS

010637	Ring, scraper, 3 1/4 in. by 1/8 in	1	G80S

010650	Pin, gudgeon	1	G3LS

010651	Pin, gudgeon	1	G80S

000750	Circlip, for gudgeon pin	2	All singles

018948	Piston, complete, .020 oversize	1	G3LS

018949	Piston, complete, .040 oversize	1	G3LS

018950	Piston, complete, .020 oversize	1	G80S

021392	Piston, complete, .040 oversize	1	G80S

018929	Piston, bare, .020 oversize	1	G3LS

018930	Piston, bare, .040 oversize	1	G3LS

018932	Piston, bare, .020 oversize	1	G80S

021391	Piston, bare, .040 oversize	1	G80S

018280	Ring, compression, 2 23/32 in. plus .020 in. By 1/16 in. (Chrome plated)	1	G3LS

018281	Ring, compression, 2 23/32 in. plus .040 in. By 1/16 in. (Chrome plated)	1	G3LS

016443	Ring, compression, 2 23/32 in. plus .020 in. By 1/16 in.	1	G3LS

016444	Ring, compression, 2 23/32 in. plus .040 in. By 1/16 in.	1	G3LS

016445	Ring, scraper, 2 23/32 in. plus .020 in. By 1/in.	1	G3LS

016446	Ring, scraper, 2 23/32 in. plus .040 in. By 1/in.	1	G3LS

016449	Ring, compression, 3 1/4 in. plus .020 in. by 1/16 in. (Chrome plated)	1	G80S

016450	Ring, compression, 3 1/4 in. plus .040 in. by 1/16 in. (Chrome plated)	1	G80S

013661	Ring, compression, 3 1/4 in. plus .020 in. by 1/16 in.	1	G80S

016447	Ring, compression, 3 1/4 in. plus .040 in. by 1/16 in.	1	G80S

013662	Ring, scraper, 3 1/4 in. plus .020 in. by 1/8 in.	1	G80S

016448	Ring, scraper, 3 1/4 in. plus .040 in. by 1/8 in.	1	G80S

022560	Flywheel, bare, driving side	1	G3LS

022561	Flywheel, bare, driving side	1	G80S

021245	Flywheel bare. timing side	1	G3LS

021246	Flywheel, bare, timing side	1	G80S

021247	Axle, timing side flywheel	1	G3LS,G80S

024132	Axle, driving side flywheel	1	G3LS,G80S

000573	Key, driving side flywheel axle	1	All singles

021249	Nut, timing side flywheel axle	1	G3LS,G80S

000234	Nut, driving side flywheel axle	1	G3LS,G80S

010312	Rod, connecting with liner and bush	1	G3LS,G80S

017400	Liner for big-end bearing	1	G3LS,G80S

017317	Bush, for gudgeon pin	1	All singles

017020	Crankpin, only	1	G3LS,G80S

000075	Roller, for crankpin, 1/4 in. by 1/4 in	30	G3LS,G80S

010395	Cage, for crankpin rollers	1	G3LS,G80S

000233	Nut, for crankpin	2	G3LS,G80S

024344	Crankcase, complete	1	G3LS,G80S

024346	Crankcase, driving side only	1	G3LS,G80S

022710	Crankcase, timing side only	1	G3LS,G80S

022538	Filter, magnetic	1	All singles

000182	Washer, magnetic filter	1	All singles

000485	Screw, plug, for crankcase oil holes, 1/4 in. by 1/4 in. by 26	3	All singles

000203	Washer, fibre, for  oil hole screws	3	All singles

000300	Stud, for cylinder base, 1 25/32, in. by 3/8 in. by 26 and 20	4	G3LS,G80S

000577	Peg, dowel, locating timing gear cover	2	All singles

024016	Timing case	1	G3LS,G80S

017182	Washer, paper, for timing gear cover	1	All singles

000482	Screw, fixing timing gear cover, 1-1/16 in. by 1/4 in. by 26	5	All singles

000765	Cap, in timing gear cover, for cam bush	1	All singles

024018	Cover, timing case	1	G3LS,G80S

000453	Screw, fixing timing case	2	G3LS,G80S

024159	Grommet, timing case. cover	1	G3LS,G80S

000486	PIug, oil return	1	All singles

021962	Bush, timing side flywheel axle	1	G3LS,G80S

012233	Peg, securing timing side bush	1	All singles

021872	Ball bearing, inner, for driving side axle. in. by 2 1/2 in. by 3/4 in	1	All singles

017191	Ball bearing, outer, for driving side axle, in. by 2 1/4 in. by 5/8 in	1	All singles

021859	Washer, spacing, between ball bearings	1	All singles

000651	Bush, for exhaust cam, in crankcase	1	All singles

000651	Bush, for exhaust cam, in timing case	1	G3LS,G80S

000651	Bush, for inlet cam, in crankcase	1	All singles

024329	Bush, for inlet cam, in timing case	1	G3LS,G80S

024287	Seal, oil for inlet cam, in timing case	1	G3LS,G80S

024208	Engine plates, front, bare	2	G3LS,G80S

024019	Engine plates, rear, bare	2	G3LS,G80S

024252	Cover, for engine plates	1	G3LS,G80S

000277	Stud, crankcase, bottom front	1	All singles

000288	Stud, crankcase bottom rear	1	All singles

000303	Stud, front engine plates (through frame)	1	G3LS,G80S

000278	Stud, front engine plates, top	1	G3LS,G80S

000278	Stud, front engine, plates, bottom	1	All singles

000278	Stud, rear engine plates (through crankcase), top	1	All singles

014147	Stud, rear engine plates (through crankcase), bottom	1	All singles

024276	Stud, rear engine plates, centre	1	G3LS,G80S

000004	Nut, for 5/16 in. studs	1I	All singles

000003	Nut, for 3/8 in. stud	2	All singles

000011	Washer, for 5/16 in. stud	1I	All singles

000010	Washer, for 3/8 in. stud	2	All singles

000002	Nut, for centre stud	2	All singles

000009	Washer, for centre stud	2	All singles

012967	Plunger, oil pump	1	All singles

010138	Screw, guide, oil pump plunger	1	All singles

010079	Pin, guide screw, oil pump plunger	1	All singles

000773	Cap, front end, oil pump	1	All singles

000772	Cap, rear end oil pump	1	All singles

000582	Washer, paper, pump end cap	2	All singles

000015	Screw, fixing front end cap, oil pump, 3/8 in. by 3 BA	4	All singles

000591	Bolt, fixing rear end cap, oil pump, 5/16 in. by 3 BA	4	All singles

000836	Body, release valve	1	All singles

000835	Diaphragm, for release valve	1	All singles

012695	Camshaft, exhaust	1	G3LS,G80S

016847	Washer, shim, .005 in. thick, for exhaust camshaft	1	All singles

016848	Washer, shim, .010 in. thick, for exhaust camshaft	1	All singles

024147	Camshaft, inlet	1	G3LS,G80S

017195	Pinion, timing, on flywheel axle	1	All singles

000570	Key, for timing pinion	1	All singles

000221	Nut, retaining timing pinion to axle (left hand thread)	1	All singles

010950	Tappet, bare	2	G3LS,G80S

010944	Guide, for tappet	2	G3LS,G80S

018314	Rod, long, push complete	2	G3LS

018315	Rod, long, push, complete	2	G80S

018168	Rod, long: push, bare	2	G3LS

015511	Rod, long push bare	2	G80S

000721	End, ball, bottom of long push rod	2	All singles

018266	Sleeve, tapped, top of long push rod	2	All singles

000592	Screw, adjusting, top of long push rod	2	All singles

000216	Nut, push rod adjusting screw	2	All singles

022288	Tube, cover, for long push rod	2	G3LS,G80S

010672	Gasket. rubber, top of cove, tube	2	G3LS,G80S

016944	Washer, metal, 3/64 in. thick, located below 010672	2	G3LS,G80S

011087	Washer, metal, 3/64 in. thick, located over 010672	2	G3LS,G80S

011087	Washer, metal, 3/64 in. thick, located over 010672 when compression plate fitted (two in each location)	4	G3LS

014603	Washer, metal, 1/8 in. thick, located over 010672 when compression plate fitted	2	G80S

000691	Gland, rubber, bottom of cover tube	2	All singles

022142	Rocker box, assembled	1	G3LS,G80S

014364	Rocker box, with bushes	1	G3LS,G80S

013958	Rocker box, bare	1	G3LS,G80S

013984	Gasket, for rocker box	1	All singles

017103	Bush, for rocker box	4	All singles

013980	Cover, side, for rocker box	1	G3LS,G80S

018890	Plugs, metering	3	All singles

014229	Fillet, rubber, rocker box side cover	1	All singles

000251	Stud, fixing rocker box side cover	3	All singles

000623	Nut, for rocker box side cover stud	3	All singles

000205	Washer, fibre, for rocker box side cover stud	3	All singles

000508	Union, oil, in rocker box	1	All singles

015353	Bolt, fixing rocker box, short, 1 15/16 in. By 5/16 in. by 22	4	All singles

015354	Bolt, fixing rocker box, long, 2-15/16 in. By 5/16 in. by 22	2	All singles

015355	Bolt, fixing rocker box, long, 2 3/4 in. by 5/16 in. by 22 with extension 5/16 in. by 26	2	G3LS,G80S

021444	Bolt, fixing rocker box, with extension	2	All singles

015356	Bolt, fixing rocker box, centre position, 3 5/16 in. by 5/16 in. by 22	1	All singles

000011	Washer, plain, rocker box fixing bolts	9	All singles

017192	Axle, rocker	2	All singles

017292	Sleeve, for rocker axle	2	All singles

022136	Arm, rocker, valve end, inlet	1	All singles

022137	Arm, rocker, valve end, exhaust	1	All singles

013948	Arm, rocker, tappet end, inlet and exhaust	2	All singles

000010	Washer, plain, for rocker axle	4	All singles

000003	Nut, for rocker axle	4	All singles

012722	Ring, felt, for rocker axle sleeve	2	All singles

013969	Lever, exhaust lifter	1	All singles

014523	Ring, sealing, for valve lifter lever	1	All singles

013970	Spring, for valve lifter lever	1	All singles

000451	Screw, anchor valve lifter spring, 1/2 in. by 2 BA	1	All singles

000039	Washer, plain valve lifter spring screw	1	All singles

014373	Stay, for rocker box	1	All singles

000004	Nut, fixing stay to rocker box bolt extension	2	All singles

000011	Washer, plain, rocker box. bolt extension	2	All singles

010970	Clip, for rocker box stay	1	All singles except G3CT

000364	Bolt. for rocker box stay clip, 15/16 in. by 5/16 in. by 26 	1	All singles

000011	Washer, plain rocker box stay clip bolt	1	All singles

000004	Nut, rocker box stay clip bolt	1	All singles

000011	Washer, rocker box stay	R	All singles

023447	Pipe, exhaust, bare	1	G3LS

022323	Pipe, exhaust, bare	1	G80S

021916	Support, for exhaust pipe	1	G3LS,G80S

000362	Bolt, for exhaust pipe support	1	G3LS,G80S

000192	Washer, spring. for support bolt	1	G3LS,G80S

000011	Washer, plain, support fixing bolt	1	G3LS,G80S

021887	Silencer, bare	1	G3LS

021888	Silencer, bare	1	G80S

016768	Bolt. silencer to frame	1	G3LS,G80S

000004	Nut, silencer to frame bolt	1	G3LS,G80S

000011	Washer, plain, silencer to frame bolt	1	G3LS,G80S

000192	Washer spring, silencer to frame bolt	1	G3LS,G80S

017152	Clip, clamping silencer to exhaust pipe	1	All 350

000745	Clip, clamping silencer to exhaust pipe	1	All 500

000363	Bolt. for silencer clip	1	All singles

000174	Washer, for silencer clip bolt	1	All singles

000004	Nut, for silencer clip bolt	1	All singles

024345	Crankcase, complete (Matchless)	1	All M twins

024347	Crankcase, driving side only	1	All twins

022662	Crankcase, timing side only	1	All twins

015670	Web. centre. with cap, studs, washers and nuts (no bearing and thrust washers)	1	All twins

022834	Cover, for timing gear	1	All M twins

011826	Stud. fixing centre web. 1 15/64 in. by 1/4, in. by 26 and 20	6	All twins

000012	Washer. plain. for centre web top fixing studs	2	All twins

000012	Washer, plain, for centre web centre fixing studs	2	All twins

000012	Washer, plain, for centre web bottom fixing studs	2	All twins

011843	Nut, for centre web fixing studs	6	All twins

015667	Stud. for centre web bearing cap, 2 11/16 in. by 3/8 in. By 20 and 20	2	All twins

000010	Washer, plain, for centre web bearing cap stud	2	All twins

016845	Nut, for centre web bearing cap stud	2	All twins

011628	Stud. in driving side crankcase, for cylinder and head, 5 7/16 in. by 5/16 in. by 26 and 22	4	All twins

011628	Stud, in timing side crankcase. for cylinder and head 5 7/16 in. by 5/16 in. by 26 and 22	4	All

011834	Stud, in timing side crankcase. for pump carrying plate, 1 5/8 in. by 5/16 in. by 26 and 22	3	All twins

000272	Stud. in timing side crankcase, for fixing magneto 1 1/4 in. by 5/16 in. by 26 and 22,	2	All twins

011803	Stud, in timing side crankcase. for dynamo strap, 1 13/16 in. by 1/4 in. by 26 and 20	1	All twins

021508	Shaft. in timing side crankcase, for Intermediate gear...	1	All twins

011820	Screw, retaining timing gear cover	10	All twins

011652	Adaptor. to accommodate oil feed and return pipe retaining banjo pins. 	2	All twins

011657	Washer, fibre, for banjo pin adaptors	2	All twins

010474	Bush, plain, for camshafts (in driving side crankcase)	2	All twins

011654	Bush. flanged, for camshafts. (in timing side crankcase)	4	All twins

016472	Tunnel, for camshaft chamber (fits between crankcase halves)	2	All twins

011648	Cap. in crankcase housing for inlet camshaft	1	All twins

023106	Washer, fibre, for crankcase housing cap	1	All twins

023254	Crankshaft, plugged, but bare	1	G9

023256	Crankshaft. plugged, but bare	1	G11

016649	Bearing, plain, for centre bearing (in halves) per pair	1	All twins

016648	Washer, thrust, for centre bearing 	2	All twins

011543	Bearing, roller, for crankshaft. 1 3/8 in. internal, 3 in. External, 11/16 in. wide.	2	All twins

014221	Connecting rod assembly. (No big end bearing)	2	All twins

014281	Stud, for connecting rod, 2 23/32 in. by 5/16 in. by 26	4	All twins

014279	Trunnion, for connecting rod	4	All twins

015279	Rivet, locating connecting rod stud	4	All twins

014904	Washer, plain, for connecting rod stud	4	All twins

014903	Nut, for connecting rod stud	4	All twins

018644	Bearing, plain, for connecting rod, top or bottom half each half	4	All twins

016670	Bearing, plain, for centre bearing, .010 in. undersize(2 halves)	1	All twins

016671	Bearing, plain, for centre bearing, .020 in. undersize(2 halves)	1	All twins

016672	Bearing, plain, for centre bearing, .030 in. undersize(2 halves)	1	All twins

018564	Bearing, plain, for connecting rod', .010 in. undersize, top or bottom. each half	4	All twins

016565	Bearing, plain, for connecting rod, .020 in. undersize, top or bottom, each half	4	All twins

018566	Bearing, plain, for connecting rod, .030 in. undersize, bottom, each half	4	All twins

022230	Cylinder, barrel only	2	G9

022231	Cylinder, barrel only	2	G11

022233	Washer, paper, for cylinder base	2	All twins

022598	Piston, bare, normal size	2	G9

022226	Piston, bare, normal size 	2	G11

022669	Piston, bare, .020 in. oversize	2	G9

022670	Piston, bare. .020 in. oversize	2	G11

022671	Piston, bare, .040 in. oversize	2	G9

022672	Piston, bare, .040 in. oversize	2	G11

022663	Piston, complete, normal size	2	G9

022664	Piston, complete, normal size	2	G11

022665	Piston, complete, .020 in. oversize	2	G9

022666	Piston: complete, .020 in. over-size	2	G11

022667	Piston complete, .040 in. oversize	2	G9

022668	Piston, complete, .040 in. oversize	2	G11

018297	Ring, compression, chrome plated, normal size	2	G9

022228	Ring, compression, chrome plated, normal size	2	G11

018298	Ring, compression, chrome plated, .020 in. oversize	2	G9

022315	Ring. Compression, chrome: plated .020 in. oversize ...	2	G11

018299	Ring, compression, chrome plated: .040 in. oversize	2	G9

022316	Ring compression, chrome plated, .040 in. oversize	2	G11

010631	Ring: compression, normal size	2	G9

022227	Ring, compression, normal size	2	G11

015522	Ring, compression, .020 in. oversize	2	G9

022317	Ring, compression, .020 in. oversize	2	G11

016441	Ring, compression, .040 in. oversize	2	G9

022318	Ring, compression, .040 in. oversize	2	G11

018366	Ring, scraper, normal size	2	G9

022229	Ring, scraper, normal size	2	G11

022677	Ring, scraper, .020 in. oversize	2	G9

022319	Ring, scraper, .020 in. oversize	2	G11

022679	Ring, scraper, .040 in. oversize	2	G9

022320	Ring, scraper, .040 in. oversize	2	G11

011731	Pin, gudgeon	2	G9

022277	Pin, gudgeon	2	G11

014283	Circlip, gudgeon pin	4	All twins

023019	Head, for cylinder, with valve guides, valve guide circlips and manifold studs, left	1	G9

023582	Head, for cylinder, with valve guides, valve guide circlips and manifold studs, right	1	G11

023020	Head, for cylinder, with valve guides, valve guide circlips and manifold studs, right	1	G9

023581	Head, for cylinder, with valve guides, valve guide circlips and manifold studs, left 	1	G11

022236	Gasket, for cylinder head	2	All twins

014163	Valve, inlet	2	G9

023403	Valve, inlet	2	G11

014165	Valve, exhaust	2	All twins

024131	Spring, inner, for valve	4	All twins

011769	Spring, outer, for valve	4	All twins

014169	Seat, for valve spring	4	All twins

014168	CoIlar, for valve spring	4	All twins

014167	Collet, for valve stems (in pairs)	4	All twins

014170	Guide, for inlet valves	2	All twins

014171	Guide, for, exhaust valves	2	All twins

011111	Circlip, locating valve guides	4	All twins

011634	Spacer, 25/32 in. long, for head retaining nuts	8	All twins

000004	Nut, retaining cylinders and heads	8	All twins

000011	Washer, plain, for head retaining nut	8	All twins

010625	Stud, retaining inlet manifold, 1 11/16 in. By-1/4 in. By 26 and 2O	4	All twins

014352	Bush, for rocker spindle	4	All twins

018961	Camshaft, inlet	1	All twins

018962	Camshaft, exhaust	1	All twins

011620	Gear, on camshaft, 60 teeth	2	All twins

000573	Key, locating camshaft gear	2	All twins

011653	Nut, retaining camshaft gears	2	All twins

016209	Pinion, on crankshaft, 30 teeth	1	All twins

016210	Spacer, 7/32 in. long, for crankshaft pinion	1	All twins

000573	Key, locating crankshaft pinion	1	All twins

011776	Bolt, retaining crankshaft pinion, threaded 1/2 in. by 20	1	All twins

010589	Washer, plain, for crankshaft pinion bolt	1	All twins

021506	Gear, intermediate, with bush, 60 teeth	1	All twins

022016	Bush, for intermediate gear	1	All twins

018576	Follower, for camshaft	4	All twins

011626	Spindle, for camshaft followers	2	All twins

022102	Spacer, 1 19/32 in. long between camshaft followers	2	All twins

022017	Rocker, with bushes, (left inlet and right exhaust)	2	All twins

022018	Rocker, with bushes (right inlet and left exhaust)	2	All twins

014222	Spindle, for rockers	4	All twins

014226	Washer, spring, double coil, for rocker spindle	4	All twins

014275	Washer, plain, for either side of rocker spindle spring washer	8	All twins

014275	Washer, plain, for clamping end of rocker spindle	4	All twins

011760	Bolt, clamping rocker spindle. (Thread No. 2 BA)	4	All twins

015021	Washer plain for rocker spindle clamping bolt	4	All twins

011846	Nut, for rocker, spindle clamping bolt	4	All twins

014245	Bush, for, rockers. (One in each rocker)	4	All twins

019987	Bush for rockers. (One in each rocker)	4	All twins

024275	Cover, for rockers	4	G9,G11

018493	Gasket, for rocker covers	4	All twins

018492	Screw retaining rocker covers	8	All twins

018517	Rod. push, assembled with ends	4	All twins

018508	Rod, push, bare	4	All twins

015518	End, upper, for push rod	4	All twins

018519	End, lower, for push rod	4	All twins

024216	Plate, engine steady	1	All twins

000365	Bolt, securing rear of steady stay, 1 1/16 in. by 5/16 in. by 26	2	All twins

000192	Washer, spring, for steady stay frame front bolt	1	All twins

014779	Washer, lock, for steady stay frame front bolt	1	All twins

022083	Nut, for steady stay rear bolt	2	All twins

000366	Bolt, securing steady stay to frame, 1 1/4 in. by 5/16 in. by 26	1	All twins

000004	Nut, for steady stay to frame securing bolt	1	All twins

000011	Washer, plain, under heads of rear bolts	2	All twins

000192	Washer, spring, for rear bolts	2	All twins

018037	Oil pumps complete, assembled on carrying plate	1	All twins

015017	Plate, carrying, oil pumps, bare	1	All twins

014903	Nut, securing pump carrying plate to timing side crankcase	3	All twins

000011	Washer, plain, for pump carrying plate fixing nuts	3	All twins

000021	Ball , 1/4 in. steel, for return pump bleed valve	1	All twins

000701	Spring for return pump bleed valve ball	1	All twins

015001	Screw, securing return pump bleed valve spring.(Grub screw, 1/4 in. long by 5/16 in. by 22)	1	All twins

016137	Gasket, oval, behind pump carrying plate	2	All twins

016138	Gasket, round, behind pump carrying plate	1	All twins

015568	Body, oil feed pump, for 1/4 in. gears with 7/16 in. shaft	1	All twins

015599	Pin, dowel, for oil feed pump	2	All twins

015576	Plate, front end, for oil pump feed body	1	All twins

015573	Plate, back end, for oil pump feed body	1	All twins

011617	Washer, paper, between oil feed pump and carrying plate	1	All twins

000453	Screw, retaining oil feed pump to carrying plate. 1 in. by 2 BA	3	All twins

015579	Gear, driving, for oil feed pump, 1/4 in. Wide 7/16 in. shaft	1	All twins

015580	Gear, driven, for oil feed pump, 1/4 in. wide 7/16 in. shaft	1	All twins

015567	Body, oil return pump, for 3/8 in. gears with 7/16 in. shaft	1	All twins

015599	Pin, dowel, for oil return pump	2	All twins

015576	Plate, front end, for oil pump return body	1	All twins

015573	Plate, back end, for oil pump return body	1	All twins

011617	Washer, paper, between oil return pump and carrying plate	1	All twins

000453	Screw, retaining oil return pump to carrying plate, 1 in. by 2 BA	3	All twins

015577	Gear, driving, for oil return pump, 3/8 in. wide. 7/16 in. shaft	1	All twins

015578	Gear, driven, for oil return pump, 3/8 in. wide. 7/16 in. shaft	1	All twins

014235	Filter, felt. for engine crankcase	1	All twins

018120	Seat, for oil felt filter	1	All twins

014240	Valve, relief, for oil felt filter	1	All twins

014241	Spring, for oil felt filter relief valve	1	All twins

023331	Cap, assembled, oil felt filter housing (also accommodates oil non-return valve)	1	All twins

023106	Washer, oil filter housing cap	1	All twins

015034	Gasket, paper oil filter chamber (fits between the two crankcase halves)	1	All twins

022538	Filter, magnetic	1	All twins

000182	Washer, for magnetic filter	1	All twins

022385	Distributor, oil	1	All twins

014247	Cap, housing, for oil distributor	1	All twins

023106	Washer, fibre, for oil distributor housing cap	1	All twins

022580	Washer, sealing crankcase bolt	1	All twins

018747	Magneto, complete, Type K2F (Lucas number 42230-A)	1	G9,G11

458367	Pickup, with brush and spring, right	1	All twins

458368	Pickup, with brush and spring, left	1	All twins

470534	Contact breaker, complete	1	All twins

470609	Contact set	1	All twins

459037	Cover for contact breaker with switch	1	G9,G11

010339	Gasket, for magneto flange	1	All twins

000365	Bolt, retaining magneto, 1 1/16 in. by 5/16 in. by 26	1	All twins

014779	Washer, lock, for magneto retaining bolt and studs	3	All twins

000004	Nut, for magnet. retaining bolt and studs	3	All twins

014464	Gear, on magneto shaft	1	All twins

140074	Washer, plain, on magnet. shaft	1	All twins

171284	Nut, on magneto shaft, retaining magneto driving shaft	1	All twins

011833	Dynamo, Type E3L-L-1-0 (Lucas number 20009-B)	1	All twins

200826	Cover assembly	1	All twins

200737	Brush, for dynamo, set of two, per set	1	All twins

014141	Gasket, between dynamo and crankcase	1	All twins

011801	Strap, retaining dynamo to crankcase	1	All twins

014796	Screw, retaining lower end of dynamo strap to crankcase 7/16 in. by 1/4 by 20	1	All twins

000012	Washer plain, for dynamo strap retaining screw	1	All twins

010604	Crosshead, in eye of dynamo retaining strap	1	All twins

011802	Nut, tensioning dynamo strap 	1	All twins

000012	Washer, plain, for dynamo strap tensioning nut	1	All twins

011800	Gear on dynamo shaft	1	All twins

000572	Key, locating dynamo shaft gear	1	All twins

111700	Bolt, retaining gear on dynamo shaft	1	All twins

188378	Washer, lock, for dynamo gear retaining bolt	1	All twins

016850	Stud, drawing dynamo to crankcase, passing through timing cover, 2 1/2 in. long by 2 BA	1	All twins

016851	Nut, for dynamo draw stud	1	All twins

014292	Bolt, clamping crankcase throat, 3 11/16 in. by 5/16 in. by 22.	3	All twins

000011	Washer, plain, for 014292 crankcase bolts	2	All twins

013944	Plate, engine front. right side	1	All twins

013943	Plate, engine front, left side	1	All twins

000306	Stud, passing through crankcase and upper holes in engine, front plates.	1	All twins

000003	Nut, for engine plate stud	2	All twins

000278	Stud, passing through crankcase and lower holes in engine front plates, 4 9/16 in. 5/16 in. by 26	1	All twins

000011	Washer, plain, for 000278 engine plate stud	2	All twins

000004	Nut, for 000278 engine plate stud	2	All twins

000277	Stud, passing through crankcase at bottom, 4 3/8 in. by 5/16 in. by 26	1	All twins

000011	Washer, plain, for 000277 crankcase stud	2	All twins

000004	Nut for 000277 crankcase stud	2	All twins

000306	Stud, passing through front of main frame and top of engine front plate	1	All twins

000003	Nut, for 000303 frame stud	2	All twins

022291	Plate, engine, rear left	1	All except G11CS

022292	Plate, engine, rear right	1	All except G11CS

022422	Cover, rear engine plates	1	All twins

000278	Stud, passing through top of engine rear plates and the crankcase 4 9/16 in. by  5/16 in. by 26	1	All twins

000278	Stud, passing through bottom of engine rear plates and the crankcase, 4 9/16 in. by 5/16 in. by 26	1	All twins

000011	Washer, plain, for 000278 studs	3	All twins

000004	Nut, for 000278 studs	3	All twins

024276	Stud. passing through engine rear plates, rear of crankcase, and centre of front chaincase	1	All twins

000009	Washer, plain, for 024276 stud	2	All twins

000002	Nut, for 024276 stud	2	All twins

000303	Stud, passing through top of engine, rear plates, and lower end of main frame seat tube	1	All twins

000003	Nut, for 000306 stud	2	All twins

000010	Washer, for 000306 stud	1	All twins

000278	Stud, passing through back ends of engine rear plates, 4 9/16 in. by 5/16 in. by 26	2	All twins

000011	Washer, plain. for 000278 stud	4	All twins

000004	Nut, for 000278 stud	3	All twins

023508	Pipe, exhaust, bare, left side	1	G9-G11 only

023507	Pipe, exhaust, bare, right side	1	G9-G11 only

021916	Support, for exhaust pipe, left side or right side	2	G9-G11

000362	Bolt. fixing exhaust pipe to support	2	G9-G11

000011	Washer, plain, for exhaust pipe fixing bolt	2	G9-G11

000192	Washer, spring, for exhaust pipe fixing bolt	2	G9-G11

021890	Silencer, bare, left side	1	G9-G11

021891	Silencer, bare, right side	1	G9-G11

017152	Clip, clamping silencer to pipe	2	G9-G11

000363	Bolt, for silencer clip, 3/4 in. by 5/16 in. by 26	2	G9-G11

000174	Washer, plain for silencer clip bolt	2	G9-G11

000004	Nut for silencer clip bolt	2	G9-G11

016768	Stud, fixing silencer to frame	2	G9-G11

000011	Washer, plain, for silencer to frame fixing bolt	2	G9-G11

000192	Washer, spring, for silencer to frame fixing bolt	2	G9-G11

000004	Nut, silencer to frame stud	2	G9-G11

021873	Carburetter, complete, less controls(Type 376/5)	1	G3LS

021874	Carburetter, complete, less controls (Type 389/1)	1	G80S

021875	Carburetter, complete, less controls (Type 376/6)	1	G9

023595	Carburetter, complete, less controls (Type 376/78)	1	G11

021346	Spacer, for carburetter, 3/4 in. wide, 1 1/16 in. bore	1	G3LS

021252	Spacer, for carburetter, 3/4 in. wide, 1 5/32 in. bore	1	G80S

023496	Spacer, for carburetter	1	G9-G11

011633	Inlet manifold, bare	1	G9

023406	Inlet manifold, bare	1	G11

000581	Gasket, for carburetter spacer	1	G3LS,G80S

023012	Gasket, between manifold and cylinder head	2	G9-G11

018503	Ring, sealing, rubber, carburetter flange	1	All

000012	Washer, manifold retaining studs	4	G9-G11

000005	Nut, manifold retaining studs	4	G9-G11

010624	Stud, retaining carburetter to manifold	2	G9-G 11

000011	Washer, carburetter retaining studs	2	G9-G 11

000004	Nut, carburetter retaining studs	2	G9-G11

376/003	Carburetter body	1	G3LS-G11

376/002	Carburetter body	1	G9

389/003	Carburetter body	1	G80S

376/077	Side cover	1	All

376/078	Side cover jointing washer	1	All

376/079	Side cover screw	3	All

376/083	Float	1	All

376/094	Bush, for float spindle	1	All

376/089	Float needle	1	All

376/088	Float needle	1	All

376/065	Mixing chamber cap securing ring	1	G3LS,G9,G11

389/065	Mixing Chamber cap securing ring	1	G80S

4-235	Mixing chamber cap securing ring spring	1	G3LS,G9,G11

29-201	Mixing chamber cap securing ring spring	1	G80S

4-241	Screw securing fixing cap ring clip	1	All

376-064	Mixing chamber cap	1	G3LS,G9,G11

389-064	Mixing chamber cap	1	G80S

4-035	Control cable adjuster	2	All

376-062	Air valve	1	G3LS,G9,G11

389-062	Air valve	1	G80S

6-047	Air valve guide	1	G3LS,G9,G11

29-057	Air valve guide	1	G80S

376-060	Throttle valve, size 3 1/2	1	G3LS,G11

376-060	Throttle valve, size 4	1	G9

389-060	Throttle valve, size 3 1/2	1	G80S

4-046	Air valve spring	1	All

376-061	Throttle valve spring	1	G3LS,G9,G11

389-061	Throttle valve spring	1	G80S

376-068	Throttle stop screw	1	All

376-069	Throttle stop screw spring	1	All

332-017	Pilot air adjusting screw	1	All

4-148	Pilot air adjusting screw spring	1	All

376-063	Taper jet needle	1	G3LS,G9,G11

389-063	Taper jet needle	1	G80S

4-230	Taper needle clip	1	All

376-072	Needle jet, .1065	1	All

376-100	Main jet, size 210	1	G3LS

376-100	Main jet, size 260	1	G80S

376-100	Main jet, size 220	1	G9

376-100	Main jet, size 280	1	G11

376-073	Main jet holder	1	All

376-074	Jet holder washer	1	All

376-075	Main jet cover	1	All

376-076	Pilot, jet, size 30	1	All

376-095	Pilot jet cover nut	1	All

116-162	Pilot jet cover nut washer	1	All

376-057	Jet block, 1 1/16 in.	1	G3LS,G11

376-056	Jet block, 1 in.	1	G9

389-057	Jet block, 1 5/32 in	1	G80S

376-067	Jet block washer	1	All

376-070	Locating peg for jet block	1	All

376-097	Petrol pipe banjo	1	All

376-091	Petrol pipe banjo bolt	1	All

376-092	Petrol pipe banjo bolt washer	1	All

14-175	Banjo seating washer	1	All

376-093	Filter gauze	1	All

343-011	Tickler Body	1	All

376-086	Tickler plunger	1	All

376-087	Tickler spring	1	All

376-066	Air intake venturi	1	G3LS,G9,G11

389-066	Air intake venture	1	G80S

022346	Cleaner, air	1	G3LS,G80S,G9,G11

022348	Hose, for air cleaner	1	G3LS,G80S

022347	Hose, for air cleaner	1	G9,G11

023273	Clip, retaining air cleaner hose	1	G3LS,G9,G11

023272	Clip retaining air cleaner hose	1	G80S

000347	Bolt, fixing air cleaner	1	G3LS,G80S,G9,G11

000005	Nut, for fixing bolt	1	G3LS,G80S,G9,G11

000012	Washer for fixing bolt 	1	G3LS,G80S,G9,G11

024137	Sprocket, engine, bare, 17 teeth	1	G3LS,G80S

024138	Sprocket, engine, bare, 18 teeth	1	G3LS,G80S

024139	Sprocket, engine, bare, 19 teeth	1	G3LS,G80S

024140	Sprocket, engine, bare, 20 teeth	1	G3LS,G80S

024141	Sprocket, engine, bare, 20 teeth	1	G3LS,G80S

024142	Sprocket, engine, bare, 22 teeth	1	G3LS,G80S

023066	Spacer, for engine sprocket	1	All singles

024026	Spacer, for generator rotor	1	G3LS,G80S

000230	Nut, for generator rotor and engine sprocket	2	G3LS,G80S

000176	Washer, for rotor and engine sprocket nuts	1	G3LS,G80S

023263	Sprocket, engine, bare, 18 teeth	1	All twins

023264	Sprocket, engine, bare, 19 teeth	1	All twins

023265	Sprocket, engine, bare, 20 teeth	1	All twins

023266	Sprocket, engine, bare, 21 teeth (standard on G9)	1	All twins

023267	Sprocket, engine, bare, 22 teeth (standard on G11)	1	All twins

023163	Spacer (Collar), for engine sprocket	1	All twins

023260	Bolt, for engine sprocket (also houses crankcase release valve) .	1	All twins

023268	Washer, tab for engine sprocket	1	All twins

016676	Diaphragm, for crankcase release valve	1	All Mat twins

018282	Spring, for release valve diaphragm	1	All twins

016674	Plug, retaining release valve diaphragm (screws in Bolt 023260)	1	All twins

017299	Chain, front, 67 links, 1/2 in. by .305 in	1	G3LS,G9

022870	Chain, front, 68 links, 1/2 in. by .305 in	1	G80S,G11

017376	Chain, rear, 98 links, 5/8 in. by .380 in	1	G3LS,G80S

022876	Chain, rear, 97 links, 5/8 in. by .380 in	1	G9,G11

110046-26	Link, connecting, for  1/2 in. chains	R	All

110056-26	Link, connecting, for 5/8 in. chains	R	All

110046-30	Link, cranked, double, for 1/2 in. chains	R	All

110056-30	Link, cranked, double, for 5/8 in. chains	R	All

110046-27	Clip, spring, for 110046-26 connecting links (1/2in.)	R	All

110056-27	Clip, spring, for 110056-26 connecting links (5/8in.)	R	All

022509	Bolt, gear box top fitting	1	G3LS,G80S,G9,G11

000318	Stud, gearbox bottom fixing, 4 9/16 in. by 7/16 in. by 26	1	All

000002	Nut, for gearbox top fixing bolt	1	All

000002	Nut, for gearbox bottom fixing stud	2	All

000177	Washer, plain for top fixing bolt	2	All

022869	Eye-bolt, for front chain adjustment	1	G3LS,G80S

023259	Eye-bolt, for front chain adjustment	1	G9,G11

000004	Nut, for front chain adjustment eye-bolt	1	G3LS,G80S,G9,G11

022504	Crosshead, for front chain adjuster eye-bolt	1	G3LS,G80S,G9,G11

000402	Bolt, fixing crosshead to engine plate	1	G3LS,G80S,G9,G11

000010	Washer, plain, for crosshead fixing bolt	1	G3LS,G80S,G9,G11

040144	Shell, gear box, with two bushes	1	All except G3CS,G80CS

040143	Case, inner, for kick-start	1	G3LS,G80S,G9,G11

040142	Cover, outer, for kick-start	1	All

040030	Gasket, for inner kick-start case	1	All

040055	Gasket, for outer kick-start Case	1	All

040138	Plug, drain, for shell	1	All

000200	Washer, fibre, for drain plug	1	All

000348	Plug, oil level	1	All

000203	Washer, fibre, for oil level plug	1	All

040053	Cover, inspection	1	All

040057	Gasket, for inspection cover	1	All

000450	Screw, for inspection cover	2	All

000577	Pin, dowel, locating kick-start case	2	All

040064	Stud, in shell for kick-start case	2	All

000271	Stud, in shell, for kick-start case	5	All

000004	Nut. for kick-start case stud	7	All

000577	Pin, dowel, locating kick-start cover	2	All

000482	Screw, securing kick-start cover	5	All

040001	Main shaft, for gearbox	1	All

040025	Layshaft, for gearbox	1	All

040116	Gear, driving, main, with bushes, 24 teeth	1	G3LS,G80S,G9,G11

040026	Gear, first mainshaft, 14 teeth	1	G3LS,G80S,G9,G11

040418	Gear, second mainshaft, 18 teeth	1	G3LS,G80S,G9,G11

040012	Gear, third, mainshaft, 21 teeth	1	All

040284	Pinion, on layshaft, 18 teeth	1	G3LS,G80S,G9,G11

040019	Gear, second layshaft, 24 teeth	1	G3LS,G80S,G9,G11

040016	Gear, third layshaft, 21 teeth	1	All

040115	Gear, first layshaft, 28 teeth	1	G3LS,G80S,G9,G11

040062	Bush, for main driving gear	2	All

040048	Bush, for mainshaft second gear	1	All

040047	Bush, for layshaft third gear	1	All

040046	Bush, for layshaft first gear	1	All

040098	Bearing, ball, for main driving gear	1	All

040099	Bearing, ball, for mainshaft in kick-starter case	1	All

040100	Bearing, ball, for layshaft in shell	1	All

040056	Bush, in shell for camplate spindle and quadrant spindle	1	All

040132	Oil seal, for  main gear bearing	1	All

040129	Oil seal, " 0 " ring for quadrant assembly	1	All

040072	Bush, in kick-starter case, for kick-starter spindle	1	All

040061	Bush, in kick-starter case for footchange spindle	1	All

040058	Bush, in kick-starter case cover, for kick-starter spindle	1	All

040063	Bush, in kick-starter case cover, for footchange spindle	1	All

040079	Oil seal, " 0 " ring for ratchet spindle	1	All

040006	Oil seal, " 0 " for ring footchange spindle	1	All

040005	Oil seal, " 0 " ring for kick-starter	1	All

040036	Bush for cam-plate plunger	1	All

040407	Sprocket, gearbox, 16 teeth, 5/8 in. by .380 in.	1	All

040070	Nut, fixing gearbox sprocket	1	All

040076	Plate, locking gearbox sprocket nut	1	All

000450	Screw, for sprocket locking plate	1	All

040131	Spacer, for gearbox sprocket	1	All

040018	Cam-plate, only	1	All

040015	Spindle only, for cam-plate	1	All

040109	Quadrant assembly, with spindle	1	All

000174	Washer, plain, for cam-plate and quadrant	2	All

040136	Screw, for cam-plate and quadrant	2	All

040022	Fork, selector	2	All

040035	Shaft, for selector fork	1	All

040111	Gear, ratchet assembly	1	All

040078	Roller for knuckle pin	1	All

040038	Spring, pawl, for gear-change	1	All

040110	Carrier, pawl assembly	1	All

040002	Carrier, pawl only	1	All

040067	Pin, for pawl carrier	1	All

040024	Pawl, foot-change	1	All

040049	Circlip, foot-change pawl	1	All

040066	Spindle, for ratchet	1	All

040075	Spring, return, gear-change	1	All

040135	Washer, foot-change return spring	1	All

040052	Plate, stop, gear-change	1	All

041400	Screw, gear-change stop plate	1	All

014117	Washer, shakeproof, stop plate screw	1	All

041311	Pedal, foot-change, bare	1	All

040086	Rubber, only, foot-change pedal	1	All

040105	Bolt. foot-change pedal	1	All

000012	Washer, spring foot-change pedal bolt	1	All

000005	Nut, foot-change pedal bolt	1	All

040051	Indicator, gear	1	All

040137	Screw, gear indicator	1	All

000012	Washer, plain, gear indicator screw	1	All

040034	Plunger, for cam-plate	1	All

040442	Spring, for cam-plate plunger	1	All except G3CS,G80CS

040366	Centre, clutch	1	All

040353	Plate. back, for clutch	1	All

040351	Plate, race	1	All

040367	Cage, roller	1	All

000075	Roller for clutch	15	All

040392	Sprocket, with inserts, for clutch	1	All

040371	Insert, for clutch sprocket per doz.	19	All

040354	Centre, shock absorber	1	All

040386	Rubber, large, shock absorber	3	All

040387	Rubber, small, shock absorber	3	All

040362	Plate, cover, shock absorber	1	All

040363	Screw, shock absorber cover plate	3	All

040373	Nut, retaining clutch	1	All

040374	Washer, lock, for clutch retaining nut	1	All

040355	Plate, clutch, plain	4	G3LS

040355	Plate, clutch, plain	5	All except G3LS

040391	Plate, clutch, with inserts	3	G3LS

040391	Plate, clutch. with inserts	4	All except G3LS

040370	Insert, for clutch plates per doz.	60	G3LS

040370	Insert, for clutch plates per doz.	80	All except G3LS

040393	Plate, pressure, bare	1	G3LS

040365	Plate, pressure, bare	1	All except G3LS

040360	Adjuster, for clutch, in pressure plate	1	All

040376	Nut, lock, for clutch adjuster	1	All

040384	Stud, for clutch spring	3	All

040388	Cup, for clutch spring	3	All

040385	Spring, for clutch	3	All

040356	Nut, fixing clutch stud to centre	3	All

040389	Nut, for clutch spring adjustment	3	All

040084	Rod, clutch operating	1	All

040029	Lever, clutch operating	1	All

040059	Body, clutch operating	1	All

040003	Ring, lock, clutch operating body	1	All

040031	Ball, clutch operating	1	All

040060	Roller, clutch operating	1	All

040065	Sleeve, clutch operating roller	1	All

000457	Screw, clutch operating roller-2 BA	1	All

011846	Nut, clutch operating roller screw-2 BA	1	All

040114	Axle kick-starter, with bush	1	All

040146	Bush, for kick-starter axle	1	All

040017	Pawl, for kick-starter axle	1	All

040033	Pin, kick-starter axle pawl	1	All

040044	Spring, kick-starter, axle pawl	1	All

040069	Plunger, kick-starter, axle pawl	1	All

040042	Stop, for kick-starter axle	1	All

040071	Cam, for kick-starter axle	1	All

040041	Rivet, for kick-starter cam and stop	2	All

040023	Nut, for main shaft (kick-starter end)	1	All

040043	Spring, return, kick-starter	1	All

040101	Crank, kick-starter (with integral pin)	1	G3LS,G80S,G9,G11

040102	Bolt, fixing, kick-starter crank to axle	1	All

023028	Frame, front portion, only bare	1	G3LS,G80S

023029	Frame, front portion. only, bare	1	G9,G11

000806	Race, Ball, for frame head lug	2	All except G3LCT

000072	balls, 3/16 in. diameter, for steering head per set of	56	All

000051	Nipple, grease, for frame head lug	1	All

023250	Stud, for seat lug (below saddle)	1	G3LS,G80S,G9,G11

000292	Nut, for seat lug stud	2	G3LS,G80S,G9,G11

000176	Washer, for seat lug stud	2	G3LS,G80S,G9,G11

021084	Stud, uniting front frame and rails	1	G3LS,G80S,G9,G11

000003	Nut, for uniting stud	1	All

000010	Washer, for uniting stud	1	All

023036	Loop, rear frame	1	G3LS,G80S,G9,G11

022246	Rail, frame, left side	1	G3LS,G80S,G9,G11

022247	Rail, frame, right side	1	G3LS,G80S,G9,G11

022248	Stud, for rear loop at bottom	1	G3LS,G80S,G9,G11

000002	Nut. rear loop stud	2	All

000009	Washer, rear loop stud	2	All

023165	Tube, supporting rear mudguard, left side	1	G3LS,G80S,G9,G11

023166	Tube, supporting rear mudguard, right side	1	G3LS,G80S,G9,G11

000351	Bolt, fixing support tube to mudguard	2	G3LS,G80S,G9,G11

022549	Washer, chrome (outside), support tube bolt	2	G3LS,G80S,G9,G11

000191	Washer, spring support tube bolt	2	G3LS,G80S,G9,G11

000005	Nut, support tube bolt	2	G3LS,G80S,G9,G11

023269	Bolt, fixing support tube to loop (also fixes top pivot of rear leg)	2	G3LS,G80S,G9,G11

022519	Cover, for frame	1	G3LS,G80S

022390	Cover, for frame	1	G9,G11

022541	Beading, plastic, 20 in. for frame cover	1	G3LS,G80,G9,G11

014357	Screw, for frame cover	2	All

000191	Washer, spring, for frame cover screw	2	All

021543	Fork, rear	1	All

021595	Adjuster, rear chain	1	All

011373	Nut, lock, for chain adjuster	1	All

014746	Sleeve, assembly (bushed)	2	All

010116	Tube	1	All

010095	Cap, for rear fork bearing, right side	1	All

010096	Cap, for rear fork bearing, left side	1	All

010093	Washer, felt, for rear fork bearing	2	All

010098	Gasket, for rear fork bearing caps	2	All

010094	Spoke, for rear fork bearing (central tie bolt)	1	All

012472	Nipple, for rear fork bearing spoke	1	All

000485	Screw, plug, for oil, in end cap, 1/4 in. by 1/4 in. by 26	1	All

000203	Washer, fibre, for oil plug screw	1	All

022879	Pin, cotter, for bearing tube	2	All

000004	Nut, for bearing cotter pin	2	All

014117	Washer, for bearing cotter pi	2	All

023521	Fork, assembly (TELEDRAULIC Front Fork, Solo)	1	G3LS, G80S,G9,G11

023522	Fork, assembly (TELEDRAULIC Front Fork, Sidecar)	1	G3LS,G80S,G9,G11

023523	Front fork inner tube assembly, Solo	2	G3LS,G80S,G9,G11

023524	Front fork inner tube assembly, Sidecar	2	G3LS,G80S,G9,G11

021974	Front fork damper assembly	2	G3LS,G80S,G9,G11

021927	Crown, assembly, comprising crown, stem and circlip	1	G3LS,G80S,G9,G11

000805	Race, ball, for fork crown	1	All

021740	Screw, pinch, for fork crown	2	G3LS,G80S,G9,G11

021749	Lug, for handlebar and steering head	1	G3LS,G80S,G9,G11

012620	Race, ball, for handlebar lug	1	All

000051	Nipple, grease, for handlebar lug	1	All

021741	Nut, adjusting, for fork crown stem	1	All

021642	Nut, lock (domed), for fork crown stem	1	All

022823	Tube, fork, inner	2	All

021911	Buffer, rubber, for fork inner tube	6	All

021495	Bush, bottom, for fork inner tube	2	All

021651	Circlip, for fork inner tube bush	4	All

022215	Bolt, top, for fork inner tube	2	All

022216	Grommet for top bolt	2	All

022213	Adaptor for damper rod	2	All

014355	Ring, sealing, for fork inner tube top bolt	2	All

022792	Slider, fork, with cap, studs and nuts, left	1	G3LS,G80S,G9,G11

022793	Slider, fork, with cap, studs, and nuts, right	1	G3LS,G80S,G9,G11

022799	Cap, for fork slider	2	All

010713	Stud securing fork slider cap, 1 13/16 in. by 5/16 in. by 26 and 22	4	All

000011	Washer, plain, for fork slider cap stud	4	All

000004	Nut, for fork slider cap stud	4	All

021907	Extension, for fork slider	2	All

022700	Bush, plastic. for fork inner tube	2	All

022699	Oil seal, for fork inner tube (rubber)	2	All

022369	Spring, main, for front fork, solo	2	G3LS,G80S,G9,G11

021789	Spring, main, for front fork, sidecar	2	G3LS,G80S,G9,G11

022079	Spring. buffer, for front fork	2	All

022021	Collar, for buffer spring	2	All

021785	Washer, leather, fork spring seating, top	2	All

021786	Washer, leather, fork spring seating, bottom	2	All

021732	Tube, fork cover, top, right, with lamp lug	1	All

021731	Tube, fork cover, top, left, with lamp lug	1	All

021742	Spigot, for top of fork top cover tubes	2	All

021910	Seat (rubber), for cover tube	2	All

021912	Housing, for fork top cover tube	2	All

021735	Tube fork cover, bottom	2	All

000485	Screw, plug, oil drain. for fork slider, 1/4 in. by 1/4 in. by 26	2	All

000203	Washer, fibre, for fork slider screw Oil	2	All

022890	Tube, fork damper	2	G3LS,G80S,G9,G11

010697	Bolt, fixing fork damper to slider, 7/16 in. by 5/16 in. by 26	2	All

010706	Washer, fibre, for damper tube bolt	2	All

017357	Rod, for fork damper	2	All

000004	Nut, lock, top end of damper rod	2	All

016072	Sleeve, plunger, for fork damper rod	2	All

016339	Clip, retaining damper rod sleeve	2	All

016304	Valve, for fork damper	2	All

010721	Pin, stop, for fork damper valve	2	All

010719	Seat, for fork damper valve	2	All

000005	Nut, lock, for fork damper valve seat	2	All

018691	Steering locking bar (own padlock to be used)	1	All

024180	Unit, complete, frame stay (Solo)	2	G3LS,G80S,G9,G11

023276	Unit complete. frame stay (Sidecar)	2	G3LS,G80S,G9,G11

024442	Unit, damper, inner assembly (Solo and Sidecar)	2	G3LS,G80S,G9,G11

023480	Dust Shield, Top	2	All except scrambles

023481	Dust shield. bottom	2	All

023479	Clips, top shield each half	4	All

023373	Spring, main, Solo (red and pink)	2	G3LS,G80S,G9,G11

023372	S ring, main, Sidecar (blue and yellow)	2	G3LS,G80S,G9,G11

023599	Sleeve, assembly, with rubber bush, top pivot	2	All

023485	Rubber, bottom pivot	2	All

023600	Bush, bottom pivot, rubber	2	All

023601	Nut, bottom pivot, bolt	2	All

023269	Bolt, top pivot	2	G3LS,G80S,G9,G11

016712	Nut, top pivot bolt	2	G3LS,G80S,G9,G11

016359	Bolt, bottom pivot	2	All

000010	Washer, plain, pivot bolts	4	All

022060	Damper steering, complete set of parts	1	All

017259	Knob, control, for steering damper	1	All Mat

000162	Washer, ratchet, for steering damper knob	1	All

000195	Washer, spring, for steering damper knob	1	All

010808	Cap. for top of steering stem	1	All

010807	Drawbolt, for steering damper	1	All

015137	Sleeve, assembly, lower end of drawbolt	1	All

000073	Nut, locking sleeve to drawbolt	1	All

014577	Bolt, fixing sleeve assembly, 7/16 in. by 1/4 in. by 26	1	All

000191	Washer, spring, for bolt 014577	1	All

000012	Washer, plain, for bolt 014577	1	All

017008	Plate, anchor, top position	1	All

014577	Bolt, fixing top anchor plate, 7/16 in by 1/4 in. by 26	1	All

000191	Washer, spring, for bolt 014577	1	All

000812	Washer, friction, for steering damper	2	All

021811	Nut, lock, for fork crown stem (replaces domed locknut 021642 if a  steering damper is fitted)	1	All

022484	Handlebar, bare (standard)	1	G3LS,G80S,G9,G11

022732	Handlebar, bare (semi-western)	1	G3LS,G80S,G9,G11

021978	Clip, (half only), for handlebar lug	1	All

016947	Screw, for handlebar clip, 7/8 in. by 1/4 in. by 26 (socket head)	3	All

016340	Stand, centre, bare	1	G3LS,G80S,

024177	Stand, centre, bare	1	G9,G11

014629	Rod, for centre stand	1	G3LS,G80S,G9,G11

000002	Nut, centre stand rod	2	All

010912	Washer, spigot, centre stand rod	2	All

014626	Bush, for centre stand	2	G3LS,G80S,G9,G11

014630	Spacer, long, centre stand rod	1	G3LS,G80S,G9,G11

014627	Spring, return, for centre stand	1	All

016399	Spring, stop, for centre stand	1	All

012565	Bolt, fixing, centre stand stop spring	2	All

000039	Washer, stop, spring bolt	2	All

014715	Stand, prop, bare	1	G3LS,G80S

014719	Stand, prop, bare	1	G9,G11

014713	Bolt, hinge, prop stand	1	All

014139	Nut, hinge, bolt	1	All

000049	Pin, split, hinge bolt	1	All

021261	Spring, return, prop stand	1	All

022372	Mudguard, front, bare	1	G3LS,G80S,G9,G11

022373	Stay, front, mudguard	1	G3LS,G80S,G9,G11

010795	Bolt, stay to fork slider	2	G3LS,G80S,G9,G11

000192	Washer, spring, stay to fork slider bolt	2	G3LS,G80S,G9,G11

000070	Bolt, stay to mudguard	2	G3LS,G80S,G9,G11

000191	Washer, spring, stay to mudguard bolt	2	G3LS,G80S,G9,G11

000012	Washer, plain, stay to mudguard bolt	2	G3LS,G80S,G9,G11

000005	Nut, stay to mudguard bolt 	2	G3LS,G80S,G9,G11

010795	Bolt, mudguard bridge to slider, right	2	All

000192	Washer, mudguard bridge bolt	2	All

010624	Stud, mudguard bridge to slider, left	2	All

000004	Nut, mudguard bridge stud	2	All

014117	Washer, shakeproof mudguard bridge stud	2	All

022684	Rear mudguard (both portions with joint bolts) (Matchless only)	1	G3LS,G80S,G9,G11

022388	Rear mudguard, forward portion only (Matchless only)	1	G3LS,G80S,G9,G11

021710	Rear mudguard, rear portion only	1	G3LS,G80S,G9,G11

021098	Bolt, for mudguard joint	3	G3LS,G80S,G9,G11

021099	Washer, for mudguard joint bolt	3	G3LS,G80S,G9,G11

022250	Bracket, for bottom of rear mudguard	2	G3LS,G80S,G9,G11

000342	Bolt, fixing bracket to rear mudguard, 11/16 in. By 1/4 in. By 26	2	G3LS,G80S,G9,G11

000012	Washer, plain, for bracket fixing bolt	4	G3LS,G80S,G9,G11

000005	Nut, for bracket fixing bolt	2	G3LS,G80S,G9,G11

000275	Stud, fixing rear mudguard brackets to frame, 3 9/16 in. By 5/16 in. by 26	1	G3LS,G80S,G9,G11

000011	Washer, plain, for bracket fixing stud	2	G3LS,G80S,G9,G11

000004	Nut, for bracket fixing stud	2	G3LS,G80S,G9,G11

000346	Bolt, fixing rear mudguard to frame loop bridge, 1 7/16 in. By 1/4 in. by 26	1	All

000191	Washer, spring, for bridge fixing bolt	1	All

000005	Nut, for bridge fixing bolt	1	All

000012	Washer, plain, for bridge fixing bolt	1	All

000172	Washer, plain, for bridge fixing bolt	1	All

011835	Plate, number, front	1	G3LS,G80S,G9,G11

011836	Stud, fixing front number plate	2	All

000012	Washer, plain, front number plate stud	2	All

000005	Nut, front number plate stud	2	All

000861	Screw, fixing front number plate to stud, 5/16 in. by 2 BA 	2	All

011889	Fillet, rubber, front number plate	1	G3LS,G80S,G9,G11

018737	Plate, number, rear, 8 in. wide	1	G3LS,G80S,G9,G11

000363	Bolt, fixing rear number plate, 3/4 in. by  5/16 in. by 26	2	G3LS,G80S,G9,G11

000192	Washer, spring, rear number plate bolt	2	G3LS,G80S,G9,G11

023233	Carrier, rear, assembled (horizontal)	1	G3LS,G80S,G9,G11

022576	Carrier, rear, assembled (inclined)	1	G3LS,G80S,G9,G11

022738	Bolt, fixing carrier	2	G3LS,G80S,G9,G11

022737	Washer, carrier fixing bolt	2	G3LS,G80S,G9,G11

024152	Chaincase, back half, assembled	1	G3LS,G80S

024153	Chaincase, back half, assembled	1	All Twins

024012	Chaincase, front half, only	1	G3LS,G80S

024008	Chaincase. front half, only	1	All Twins

024148	Screw, fixing chaincase to crankcase	3	G3LS,G80S and all Twins

022131	Washer, chaincase fixing screw	3	G3LS,G80S and all Twins

024136	Stud, chaincase centre	1	G3LS,G80S

024285	Stud, chaincase centre	1	All Twins

000004	Nut, chaincase centre stud	1	G3LS,G80S

024286	Nut, chaincase centre stud	1	All Twins

000011	Washer, chaincase centre stud	1	G3LS,G80S and all Twins

000484	Screw, joining chaincase halves	14	G3LS,G80S and all Twins

012019	Plug, drain	1	G3LS,G80S and all Twins

000200	Washer, fibre, drain plug	1	G3LS,G80S and all Twins

042040	lnspection cap	2	G3LS,G80S and all Twins

042025	Gasket, inspection cap	2	G3LS,G80S and all Twins

024020	Gasket, chaincase joint	1	G3LS,G80S

024021	Gasket, chaincase joint	1	All Twins

024024	Gasket, chaincase centre stud	1	G3LS,G80S and all Twins

024023	Gaskets, centre boss to crankcase	1	G3LS,G80S

024022	Gaskets, centre boss to crankcase	1	All Twins

024157	Chainguard, rear, only	1	G3LS,G80S

024154	Chainguard, rear, only	1	All Twins

000350	Bolt, fixing chainguard, at front	1	All

024218	Bolt, fixing chainguard at rear	1	All

023146	Nut, front fixing bolt	1	All

021578	Spacer, rear fixing bolt	1	All

021579	Washer, rear fixing bolt	1	All

023509	Washer, tab, front bolt	1	All

023102	Carrier, battery, back portion only	1	G3LS,G80S,G9,G11

023097	Carrier, battery, front strap	1	G3LS,G80S,G9,G11

000369	Bolt, battery carrier to frame	1	G3LS,G80S

000369	Bolt, battery carrier to frame	2	G9,G11

000349	Bolt, battery carrier to frame	1	G3LS,G80S,G9,G11

000004	Nut, for 000369 bolt	1	G3LS,G80S

000004	Nut, for 000369 bolt	2	G9,G11

000011	Washer, for 000004 nut	2	G3LS,G80S

000011	Washer, for 000004 nut	4	G9,G11

000005	Nut, for 000349 bolt	1	G3LS,G80S,G9,G11

000012	Washer, for 000005 nut	1	G3LS,G80S,G9,G11

014577	Bolt. earthing cable	1	G3LS,G80S,G9,G11

000012	Washer, earthing cable bolt	1	G3LS,G80S,G9,G11

022721	Rubber, for battery carrier	1	G3LS,G80S,G9,G11

018601	Arm, for footrest	2	G3LS. G80S,G9,G11

010847	Pad, rubber, for footrest arm	2	G3LS,G80S,G9,G11

018604	Rod, for footrests, overall length, 10 1/2 in.	1	G3LS,G80S,G9,G11

010924	Spacer, 3 1/2 in. long, for footrest rod, between rear engine plates	1	All

013837	Spacer, 1 in. long, for footrest, outside right	1	G3LS,G80S,G9,G11

010911	Spacer, 13/16 in. long, or footrest, outside left	1	G3LS,G80S,G9,G11

000009	Washer, plain, for footrest rod	2	All

000002	Nut, for footrest rod	2	All

021984	Pillion footrests, complete pair	1	G3LS,G80S,G9,G11

021641	Spindle, bare, pillion footrest	2	G3LS,G80S,G9,G11

011599	Bolt, hinge, for pillion footrest spindle, 1 3/16 in. by  3/8in. by 26	2	G3LS,G80S,G9,G11

000073	Nut, for pillion footrest hinge bolt	2	G3LS,G80S,G9,G11

010847	Pad, rubber, for pillion footrest spindle	2	G3LS,G80S,G9,G11

023039	Twin seat ( Matchless only)	1	G3LS,G80S,G9,G11

023251	Screw, fixing twin seat	2	G3LS,G80S,G9,G11

022083	Nut, twin seat fixing screw	2	G3LS,G80S,G9,G11

000011	Washer, twin seat fixing screw	2	G3LS,G80S,G9,G11

023300	Box, tool, bare, with lid, Matchless only 	1	G3LS,G80S,G9,G11

023327	Lid, only, for tool box (black), Matchless only	1	G3LS,G80S,G9,G11

024317	Lid, only, for tool box (red), Matchless only	1	G3LS,G80S,G9,G11

014511	Screw. knurled, for tool box lid	1	All

000189	Washer, spring, for tool box lid screw	1	All

000005	Nut, for tool box led screw	2	All

000070	Bolt, fixing tool box, top and rear	2	G3LS,G80S,G9,G11

000005	Nut, tool box fixing bolt	2	G3LS,G80S,G9,G11

000012	Washer, tool box fixing bolt	4	G3LS,G80S,G9,G11

000070	Bolt, tool box, battery carrier	2	G3LS,G80S,G9,G11

000005	Nut, tool box, battery carrier bolt	2	G3LS,G80S,G9,G11

000012	Washer, tool box, battery carrier bolt	4	G3LS,G80S,G9,G11

024416	Transfers, complete set, Matchless only	1	G3LS,G80S,G9

024419	Transfers, complete set, Matchless only	1	G11

009197	Transfer, for rear fork hinge (patent)	1	All

009199	Transfer, for front forks (patent)	1	All

009200	Transfer, for front forks (made in England)	1	All

009189	Transfer, rear mudguard (Matchless)	1	All Matchless

009188	Transfer, for side of oil tank (motif), Matchless only	1	All Matchless except G3CT

023277	Transfer, for oil tank (top level)	1	All except G3CT

023279	Transfer, for oil tank (low level)	1	All except G3CT

023136	Transfer, oil recommendation	1	All

009205	Transfer,  top of petrol tank (600cc)	1	G11 only

009188	Transfer,   for tool box lid (motif)	1	All Matchless

009195	Transfer,   for petrol tank (reserve)	1	All

023679	Cable, assembled, front brake, standard bar	1	G3LS,G80S,G9,G11

023680	Cable, assembled, front brake, Western bar	1	G3LS,G80S,G9,G11

011348	Adjuster, front brake cable	1	All

017217	Nut, lock, front brake cable adjuster	1	All

022550	Sleeve, rubber, front brake cable	1	All

024169	Cable, assembled, clutch, standard bar	1	G3LS,G80S,G9,G11

024231	Cable, assembled, clutch, Western bar	1	G3LS,G80S,G9,G11

014225	Adjuster, clutch cable	1	All

011373	Nut, lock, clutch cable adjuster	1	All

023710	Cable, assembled, valve lifter, standard bar	1	All Singles

023703	Cable, assembled, valve lifter, Western bar	1	All Singles

014225	Adjuster, valve lifter cable	1	All Singles

011373	Nut, lock, valve lifter cable adjuster	1	All Singles

024170	Cable, assembled, throttle, standard bar	1	G3LS,G9,G11

024232	Cable, assembled, throttle, Western bar	1	G3LS,G9,G11

024171	Cable, assembled, throttle, standard bar	1	G80S

024245	Cable, assembled, throttle, Western bar	1	G80S

023694	Cable, assembled, air, standard bar	1	G3LS,G9,G11

023697	Cable, assembled, air, Western bar	1	G3LS,G9,G11

023695	Cable, assembled, air, standard bar	1	G80S

023698	Cable, assembled, air, Western bar	1	G80S

018749	Cable, assembled, ignition, standard bar	1	All Twins

023701	Cable, assembled, ignition, Western bar	1	All Twins

022728	Sleeve, rubber, for control cables	2	G3LS,G80S,G9,G11

366-2	Twist grip, complete	1	All

366-001	Body, twist grip, top half	1	All

366-002	Body, twist grip, bottom half	1	All

366-004	Rotor, twist grip	1	All

376-079	Screw, fixing twist grip halves	2	All

366-007	Spring, friction	1	All

366-008	Screw, friction spring	1	All

366-006	Stop, for cable	1	All

16-070	Grip, for twist grip rotor	1	All

16-069	Grip, dummy, for left side handlebar	1	All

18-867	Lever, assembly, brake and air	1	G3LS,G80S,G9,G11

18-816	Bracket, for brake lever	1	G3LS,G80S,G9,G11

18-874	Lever, only front brake	1	All

18-087	Pin, fulcrum, front brake lever	1	All

18-053	Nut, brake lever fulcrum pin	1	All

12-594	Body, air control lever	1	All

12-556	Lever only, air	1	All

12-607	Bolt, air control lever	1	All

12-606	Cap, air control lever	1	All

12-033	Washer, spring, air lever cap	1	All

11-013	Screw, clamping bracket, long	1	G3LS,G80S,G9,G11

11-014	Screw, clamping bracket, short	1	G3LS,G80S,G9,G11

023707	Adaptor, roller, for brake cable	1	All

18-868	Lever, assembly, clutch and ignition	1	All Twins

18-875	Lever, assembly, clutch	1	All Singles

18-818	Bracket, for clutch lever	1	All Twins

18-814	Bracket, for clutch lever	1	All Singles

18-873	Lever only, clutch	1	All

18-087	Pin, fulcrum, clutch lever,	1	All

18-053	Nut, brake lever fulcrum pin	1	All

12-596	Body, only ignition lever	1	All except G3LS,G80S

12-557	Lever, only ignition	1	All except G3LS,G80S

12-607	Bolt, ignition control lever	1	All except G3LS,G80S

12-606	Cap, ignition control lever	1	All except G3LS,G80S

12-033	Washer, spring, ignition lever cap	1	All except G3LS,G80S

11-013	Screw, clamping bracket, long	1	All

11-014	Screw, clamping brake, short	1	All

12-595	Clamp, control lever bracket	1	All Single

023707	Adaptor roller, for clutch cable	1	All

18-454	Lever assembly, exhaust lifter	1	All Singles

18-161	Bracket, only exhaust lifter	1	All Singles

18-059	Lever, only exhaust lever	1	All Singles

11-014	Pin, fulcrum, exhaust lifter lever	1	All Singles

18-060	Nut, exhaust lever fulcrum pin	1	All Singles

12-040	Clamp, exhaust lever body	1	All Singles

11-014	Screw, exhaust lever body clamp	1	All Singles

021307	Tank, petrol, bare, enamelled, black 	1	G3LS,G80S

023417	Tank, petrol, bare, enamelled, black	1	G9

023418	Tank, petrol, bare, enamelled, red	1	G11

023359	Panel, chrome, left side	1	G9,G11

023358	Panel, chrome, right side	1	G9,G11

023360	Bead,  tank panel, red	2	G9

023362	Bead,  tank panel, black	2	G11

018891	Motif, for petrol tank	2	G3LS,G80S,G9,G11

018896	Seating, for petrol tank motif	2	G3LS,G80S,G9,G11

000153	Screw, petrol tank motif	4	G3LS,G80S

023371	Screw, petrol tank motif	4	G9,G11

023085	Grip. rubber, for petrol tank. left side	1	G3LS,G80S,G9,G11

023086	Grip, rubber, for petrol tank, right side	1	G3LS,G80S,G9,G11

023282	Plate, for rubber grip, left side		G3LS,G80S,G9,G11

023283	Plate, for rubber grip, right side	1	G3LS,G80S,G9,G11

000348	Bolt, fixing, knee grip plate	4	G3LS, G80S

000070	Bolt, fixing, knee grip plate	4	G9,G11

000172	Washer, plain, 1/4 in., knee grip plate bolt	4	G9,G11

000178	Washer, plain, 1/4 in., knee grip plate bolt	2	G9,G11

000639	Spacer, knee grip plate bolt	2	G9,G11

013325	Cap, filler, for petrol tank	1	G3LS,G80S,G9,G11

023274	Tap, petrol, with filter and banjo	2	G3LS,G80S,G9,G11

000908	12 1/8 in. Pipe (plastic): petrol feed	1	G3LS,G80S

000908	13 1/8 in. pipe (plastic) petrol feed	1	G9,G11

021844	“T" piece union, for feed pipe	1	All

014997	Bolt, fixing, petrol tank	4	G3LS,G80S,G9,G11

014995	Rubber, thick, petrol tank fixing bolt	4	G3LS,G80S,G9,G11

014996	Rubber, thin, petrol tank fixing bolt	4	G3LS,G80S,G9,G11

014998	Sleeve, petrol tank fixing bolt	4	G3LS,G80S,G9,G11

014999	Washer, petrol tank fixing bolt	4	G3LS,G80S,G9,G11

017051	Wire, copper, petrol tank fixing bolt (coil)	Q	G3LS,G80S,G9,G11

023157	Tank, oil, bare	1	G3LS,G80S

023155	Tank, oil, bare	1	G9,G11

023304	Cover, for oil tank, black	1	G9,G11

024319	Cover, for oil tank, red	1	G9,G11

022632	Screw, for oil tank cover	2	All Twins

000203	Washer, fibre, oil tank cover screw	2	All Twins

000012	Washer, plain, oil tank cover screw	2	All Twins

021282	Cap, filler, for oil tank	1	All

021329	Washer, oil tank filler cap	1	All

012019	Plug, drain, for oil tank	1	All

000200	Washer, fibre, oil tank drain plug	1	All

000361	Bolt, fixing, oil tank top	1	All

014779	Washer, Shakeproof, oil tank top fixing bolt	1	G3LS,G80S,G9,G11

022417	Bracket, oil tank to seat tube	1	G3LS,G80S,G9,G11

000070	Bolt, oil tank bracket to seat tube	1	G3LS,G80S,G9,G11

000012	Washer, oil tank bracket bolt	1	G3LS,G80S,G9,G11

023401	Pipe, oil feed	1	G3LS,G80S

023311	Pipe, oil feed	1	G9,G11

000950	18 in. Hose, rubber, oil feed pipe	1	G3LS,G80S

000950	22 in. Hose, rubber, oil feed pipe	1	G9,G11

015198	Filter, metal gauze, for oil feed pipe	1	All

011924	Union, oil feed pipe	1	All Singles

015528	Washer. oil feed union	1	All Singles

023309	Pipe, oil return	1	G3LS,G80S

023311	Pipe, oil return	1	G9,G11

000950	18 in. Hose, rubber, oil return pipe	1	G3LS, G80S,G9,G11

023376	Ferrule. oil feed and return pipe hose	4	G3LS,G80S,G9,G11

000951	5 in. Sleeve, plastic oil feed and return pipes	1	G3LS,G80S,G9,G11

016677	Pipe, rocker box oil feed, top portion	1	All Singles

016678	Pipe, rocker box oil feed, bottom portion	1	All Singles

011381	Connection, rubber, rocker oil feed pipes	1	All Singles

000513	Nut, union, rocker feed pipe, top end	1	All Singles

017180	Nut, union, rocker feed pipe, bottom end	1	All Singles

000755	Pipe, oil discharge, for release valve	1	All Singles

022570	Pipe, vent (chain oiler)	1	All

000900	7 3/4 in. Hose, vent pipe	1	All

011649	Pin, banjo, retaining oil pipes to engine	2	All Twins

000183	Washer, fibre, oil pipe banjo	4	All Twins

024379	Wheel, front, complete with all fittings	1	G3LS,G80S ,and all Twins

024381	Wheel, front, bare, less all fittings	1	G3LS,G80S and all Twins

024248	Rim, front, 19 in. by 2 1/2 in., chrome	1	G3LS,G80S and all Twins

021152	Spoke, front wheel	40	G3LS,G80S and all Twins

021154	Nipple, front wheel spoke	40	All

024005	Hub, front wheel, shell only with brake drum	1	All

000051	Nipple. grease, front wheel hub	1	All

011090	Tape, for 19 in. by 2 1/2 in. rim	1	G3LS, G80S and all Twins

021464	Disc, for right hand side of hub	1	All

012825	Spindle, with roller bearings, for front wheel	1	All

010579	Oil seal, for front hub bearings	2	All

017219	Ring, spring, locating front hub bearings	1	All

018093	Cup, for front hub bearing oil-seal	2	All

018096	Ring, retaining front hub bearing oil-seals	2	All

021279	Nut, lock, for front hub bearing adjusting ring	1	All

021161	Ring. adjusting, for front hub bearing	1	All

021931	Nut, locating front brake cover plate	1	All

018071	Nut, outside, securing front brake cover plate	1	All

000001	Nut, front wheel spindle, left side	1	All

000008	Washer, plain, front wheel spindle, left side	1	All

024383	Wheel, rear, complete, chrome, with all fittings	1	G3LS,G80S,G9,G11

024384	Wheel, rear, bare, chrome, less all fittings	1	G3LS,G80S,G9,G11

024249	Rim, rear, 19 in. by 2 1/2 in. chrome	1	G3LS,G80S,G9,G11

021691	Spoke, rear wheel	40	G3LS,G80S,G9,G11

021693	Nipple, rear wheel spoke	40	G3LS,G80S,G9,G11

023067	Hub, rear wheel, shell only	1	G3LS,G80S,G9,G11

021582	Disc, for right hand side of hub	1	All

000051	Nipple, grease, for rear hub	1	All

011090	Tape, for 19 in. rear rim	1	All

014868	Bearings, roller, for rear hub (only sold-as a complete bearing)	2	All

014387	Oil seal, for rear hub bearings	2	All

010740	Ring, spring, locating rear hub bearings	1	All

021585	Ring, retaining rear hub bearing oil seals, small	1	All

018095	Ring, retaining rear hub bearing oil seals, large	1	All

018094	Cup, for rear hub bearing oil seal	1	All

012436	Collar, spacing, between bearing and rear hub bearing oil seal	1	All

021586	Spacer, 2 9/16 in. long between the two bearings rear hub	1	All

021583	Ring, adjusting, for rear hub bearings	1	All

021584	Nut, lock, for rear hub bearing adjusting ring	1	All

021587	Spindle, centre, solid, for rear wheel	1	All except CS

021608	Spacer, on spindle, for oil seals	1	All

021594	Spacer, on rear wheel solid spindle, for speedometer gearbox (carries nut)	1	All

021593	Nut, locking speedometer gearbox	1	All

021591	Spacer, rear wheel solid spindle (abuts against fork end), speedometer side	1	All

014869	Nut, for rear wheel solid spindle	1	All

021590	Washer, for rear wheel solid spindle	1	All

021744	Drum, front brake (must be fitted at works)	1	All

021766	Screw, fixing front brake drum to hub shell	1	All

011846	Locknut, for brake drum screw	1	All

022257	Plate, cover, front brake	1	All

021474	Stay, front brake cover plate anchor	1	All

014807	Bolt, fixing anchor stay to front cover plate, 5/8in. by 3/8in. by 26	1	All

014119	Washer, special, for anchor stay bolt	1	All

022261	Pin, fulcrum, for brake shoes	1	All

021563	Screw, front brake shoe pin	1	All

000009	Washer, plain (inner for pin)	1	All

013620	Shoes, pair of, for front brake, with brake Linings and thrust pins (only supplied in pairs)	1	All

013291	Pin, thrust, brake expander adjusting	2	All

000174	Washer, plain, for thrust pin	R	All

022832	Linings, brake, per pair of, less rivets	1	All

000113	Rivets. for brake linings per set of	14	All

012892	Spring, for brake shoes	2	All

021144	Expander, for brake shoes	1	All

017334	Washer, packing for expander bush	1	All

022260	Lever, for front brake shoe expander	1	All

000051	Nipple, grease. for brake shoe expander	1	All

000174	Washer, plain, for brake shoe expander	1	All

000004	Nut, for brake shoe expander	1	All

023070	Sprocket, and brake drum, for rear wheel, 42 teeth	1	G3LS,G80S,G9,G11

023072	Pin, driving, in hub	5	G3LS,G80S,G9,G11

023073	Bush, rear hub driving pin	5	G3LS,G80S,G9,G11

023281	Nut, rear hub driving pin	5	G3LS,G80S,G9,G11

022264	Plate, cover, rear, brake	1	All

022748	Spacer, for cover plate, outer	1	All

021605	Spacer, for cover plate. inner	1	G3LS,G80S,G9,G11

021598	Bearing, ball, for brake drum	1	G3LS,G80S,G9,G11

021599	Washer, for brake drum bearing	2	G3LS,G80S,G9,G11

021600	Circlip, for brake drum bearing	1	G3LS,G80S,G9,G11

021783	Oil seal, for brake drum bearing	1	G3LS,G80S,G9,G11

021602	spindle, dummy, for bearing	1	G3LS,G80S,G9,G11

021603	Nut, for dummy spindle	1	G3LS,G80S,G9,G11

021604	Washer, for dummy spindle	1	G3LS,G80S,G9,G11

013620	Shoes, pair of, for rear brake, with linings and thrust pins (only supplied in pairs)	1	All

013291	Pin, thrust, brake expander adjusting	2	All

000174	Washer, plain, for thrust pin	R	All

022832	Linings, brake, less rivets	1	All

000113	Rivets, for brake lining 	14	All

012892	Spring, for brake shoes	2	All

012891	Expander, for brake shoes	1	All

017113	Lever, for rear brake shoe expander	1	All Singles

021473	Lever, for rear brake shoe expander	1	G9,G11

000174	Washer, plain, for brake shoe expander	1	All

000004	Nut, for brake shoe expander	1	All

000051	Nipple, grease, for brake shoe expander	1	All

022293	Pedal, foot, for rear brake	1	G3LS,G80S

022609	Bolt, foot, pedal	1	All

021699	Fulcrum, rear, brake pedal	1	All

000051	Nipple, grease, for rear brake foot pedal	1	All

021700	Spring. return, rear brake pedal	1	All

022314	Stop, for rear brake pedal	1	All

022297	Rod, rear brake, bare	1	G3LS,G80S

023299	End, yoke, for rear end of brake rod	1	All

000736	Pin, for brake rod yoke end	1	All

000014	Pin, split, for brake rod yoke end pin	1	All

017095	Spring, for brake rod	1	All

022744	Clip. adjusting, for front end of brake rod	1	All

000736	Pin, for brake rod adjusting clip	1	All

000014	Pin, split. for brake rod adjusting cup pin	1	All

022743	Nut, adjusting, for rear brake rod	1	All

000178	Washer, brake top spring	1	All

024394	Lamp, head, with bulb, ammeter, and switch, less cable harness (home), Lucas 68135A	1	G3LS,G80S

024395	Lamp, head, with bulb, ammeter and switch, less cable harness (export, not Europe), Lucas 58136A	1	G3LS,G80S

024396	Lamp, head, with bulb, ammeter and switch. less cable harness (Europe, except France), Lucas 58137A	1	G3LS,G80S

024397	Lamp, head, less bulb, with ammeter and switch, less cable harness (France), Lucas 58138A	1	G3LS,G80S

024398	Lamp, head, with bulb, ammeter and switch, less cable harness (home), Lucas 58151A	1	G9,G11

024399	Lamp, head, with bulb ammeter and switch, less cable harness (export, not Europe), Lucas 58152A	1	G9,G11

024400	Lamp, head, with bulb, ammeter and switch, less cable harness (Europe, except France), Lucas 58153A	1	G9,G11

024401	Lamp, head, less bulb, with ammeter and switch, less cable harness (France), Lucas 58154A	1	G9,G11

516972	Shell only, top half, for headlamp	1	G3LS,G80S

516951	Shell only, top half, for headlamp	1	G9,G11

516973	Shell only, bottom half, for headlamp	1	G3LS,G80S,G9,G11

553248	Rim only, for headlamp	1	G3LS,G80S,G9,G11

144921	Screw, fixing headlamp rim	1	G3LS,G80S,G9,G11

555309	Light unit, reflector and glass (home)	1	G3LS,G80S,G9,G11

516798	Light unit, reflector and glass (export, not France)	1	G3LS,G80S,G9,G11

555275	Light unit, reflector and glass (Europe, not France)	1	G3LS,G80S,G9,G11

516802	Light unit, reflector and glass (France)	1	G3LS,G80S,G9,G11

554602	Bulb holder (all except France)	1	G3LS,G80S,G9,G11

552943	Back shell, with bulb holder (France)	1	G3LS,G80S,G9,G11

112201	Bolt, fixing lamp to fork covers	2	All

134499	Washer, headlamp fixing bolt	2	All

022126	Lamp, rear, complete (Lucas L564)	1	G3LS,G80S,G9,G11

573839	Window cover, red, for rear lamp	1	G3LS,G80S,G9,G11

575200	Window cover, white, for rear lamp	1	G3LS,G80S,G9,G11

575208	Gasket, rubber, for window cover	1	G3LS,G80S,G9,G11

552928	Screw, retaining window cover	2	G3LS,G80S,G9,G11

575207	Grommet, rubber, for bulb holder	1	G3LS,G80S,G9,G11

575209	Bulb holder	1	G3LS,G80S,G9,G11

860428	Wires, rear lamp, with Paxolin washer	1	G3LS,G80S,G9,G11

573825	Cap. rubber, covering cable entry	1	G3LS,G80S,G9,G11

166014	Nut, retaining lamp body to number plate	2	G3LS,G80S,G9,G11

188330	Washer, lamp body retaining nut	2	G3LS,G80S,G9,G11

024187	Regulator, complete unit, Type 37252	1	G9,G11

011094	Grommet, for A.V.C. cable	1	G9,G11

024204	Rubber shrouding	1	G9,G11

022720	Rubber, tool box lid	1	G9,G11

024205	Rubber, base support	1	G9,G11

022345	Battery, with lid (charged by dry), Lucas No. PUZE/9) 	1	All

4159075	Lid, only, but with rubber pads	1	All

022529	Horn, electric, with bracket	1	G3LS,G80S,G9,G11

012565	Bolt, for horn	2	G3LS,G80S,G9,G11

000080	Nut, for horn bolt	2	G3LS,G80S,G9,G11

000039	Washer, for horn bolt	4	G3LS,G80S,G9,G11

024437	Complete kit, stop light parts	1	G3LS,G80S

022002	Complete kit, stop light parts	1	G9,G11

018721	Pull off spring for switch	1	All

022032	Bracket, for switch	1	All

018764	Clip for pull off spring	1	All

000738	Screw, securing switch and pull off spring	3	All

000739	Nut for switch and pull off spring screw	3	All

000039	Washer, for switch screw	2	All

018220	Extra rubber cable clip	1	All

011908	Extra rubber cable clip	2	All

014453	Metal cable clip	1	All

024376	Cable (switch to lamp and battery), pair complete	1	G3LS,G80S

022836	Cable (switch to lamp and battery), pair complete	1	All except G3LS,G80S

900269	Snap connector (sleeve, sleeve rubber and two nipples)	1	All

022031	Switch, for stoplight	1	All

47122A	Stator, generator	1	G3LS,G80S

024150	Stud in chaincase, for generator stator	3	G3LS,G80S

011843	Nut, for generator stator stud	3	G3LS,G80S

000012	Washer, for generator stator stud	3	G3LS,G80S

041065	Grommet, rubber, for stator cable	1	G3LS,G80S

423506	Rotor, generator	1	G3LS,G80S

024026	Spacer, for rotor	1	G3LS,G80S

042195	Key, woodruff, generator rotor	1	G3LS,G80S

000230	Nut, generator rotor	2	G3LS,G80S

000176	Washer, generator rotor nut	1	G3LS,G80S

024183	Contact breaker, complete (Lucas 47578)	1	G3LS

024273	Contact breaker, complete (Lucas 47579)	1	G80S

465958	Plate, contact breaker	1	G3LS,G80S

420196	Points, contact breaker set	1	G3LS,G80S

420302	Condenser, contact breaker plate	1	G3LS,G80S

000451	Screw, fixing contact breaker plate to timing case	2	G3LS,G80S

000039	Washer, contact, plate fixing screw	2	G3LS,G80S

415729	Weight, assembly	1	G3LS,G80S

424201	Spring set, auto advance set	1	G3LS

416136	Spring set. auto advance set	1	G80S

465939	Cam, contact breaker	1	G3LS,G80S

024310	Bolt, for contact breaker cam	1	G3LS,G80S

024326	Washer, contact breaker cam bolt	1	G3LS,G80S

024327	Washer, shakeproof, contact breaker cam bolt	1	G3LS,G80S

024159	Grommet, rubber, contact breaker cable	1	G3LS,G80S

024251	Rectifier, with bolt and nut (Lucas 471 1 1 )	1	G3LS,G80S

000214	Nut. fixing rectifier	1	G3LS,G80S

014779	Washer, shakeproof rectifier fixing nut	1	G3LS,G80S

024210	Coil assembly (Lucas 45077)	1	G3LS,G80S

024212	Strap, assembly for coil	1	G3LS,G80S

024213	Screw, for coil strap	2	G3LS,G80S

024214	Seat " D ", for coil strap	4	G3LS,G80S

024215	Nut, square, for coil strap screw	2	G3LS,G80S

024404	Screw, rectifier lead	3	G3LS,G80S

024405	Nut, rectifier lead screw	3	G3LS,G80S

024406	Washer, rectifier lead screw	3	G3LS,G80S

022006	Speedometer, trip, complete, 120 m.p.h	1	G3LS,G80S,G9,G11

022010	Speedometer, trip, complete, 180 k.p.h	1	G3LS,G80S,G9,G11

021793	Head only, speedometer, 120 m.p.h	1	G3LS,G80S,G9,G11

021795	Head only, speedometer, 180 k.p.h	1	G3LS,G80S,G9,G11

53279-1	Set of bulb holding parts for speedometer head	1	All

53205	Bulb, only 6 volt, 1.8 watt m.c.b., for head	1	All

N-1253	Nut, fixing speedometer head to bracket	2	All

W-7216	Washer, speedometer head fixing nut	2	All

022057	Bracket, retaining speedometer head in headlamp	1	G3LS,G80S,G9,G11

53395-1-65	Cable, speedometer drive, complete	1	All

52108-1-65	Cable, speedometer drive, inner only	1	All

53398-1-65	Cable, speedometer drive, outer only	1	All

024448	Gearbox, for speedometer, complete	1	All

021798	Grommet, rubber, for speedometer head in headlamp	1	G3LS,G80S,G9,G11

021454	Washer, outside speedometer gearbox	1	All

021799	Grommet, rubber, for speedometer cable in fork crown	1	All

011907	Clip,  rubber, 1 11/16 in.	7	All Singles

011907	Clip,  rubber, 1 11/16 in.	4	G9,G11

011908	Clip,  rubber, 3 1/4 in	2	All

018220	Clip,  rubber, 43/in.	5	All Singles

018220	Clip,  rubber, 4 3/in.	6	G9,G11

014453	Clip,  metal, holding rear lamp cable inside mudguard	1	G3LS,G80S,G9,G11

36084	Ammeter, for headlamp	1	All

31443	Switch, for lighting and ignition	1	G3LS,G80S

31763	Switch, for lighting	1	G9,G11

351567	Handle, with screw, for lighting switch	1	G9,G11

318341	Key, for ignition switch	1	G3LS,G80S

022548	Switch, dipping, and horn button combined	1	G3LS, G80S,G9,G11

380459	Packing, rubber, for dipping switch	1	G3LS,G80S,G9,G11

021299	Screw, fixing switch to handlebar	2	G3LS,G80S G9,G11

865225	Harness cable, main lighting (no dipping or horn cable)	1	G3LS,G80S

837351	Harness, cable main lighting (no dipping, horn or regulator cables)	1	G9,G11

858795	Harness, cable, for dipping switch, triple	1	All

359218	Cable for horn	1	All

860595	Harness, cable for regulator	1	All Twins

016681	Sheath, for horn cable	1	All

000543	Cable, high tension for sparking plug	R	All

000541	Terminal, for high tension cable	R	All

900269	Connector, snap, for rear lamp and regulator cable	R	All

011094	Bush, rubber, rear lamp cable	1	All

015547	Plug, sparking, FE80 K.L.G	1	G3LS,G80S

015547	Plug, sparking, FE80 K.L.G	2	All Twins

021310	Cover, for dynamo terminals	1	All Twins

018895	Interference suppressor	R	All

312	Bulb, headlamp, main. 6 volt. 30 by 24 watt	1	G3LS,G80S,G9,G11

988	Bulb, headlamp, pilot, 6 volt. 3 watt	1	G3LS,G80S,G9,G11

384	Bulb, rear lamp, 6 volt, 18 by 6 watt, D.C	1	All

024385	Tool kit, with tyre inflator	1	G3LS,G80S

024386	Tool kit, with tyre inflator	1	All Twins

024388	Tool kit, less tyre inflator	1	G3LS,G80S

024389	Tool kit, less tyre inflator	1	All Twins

017253	Bag, for tools	1	All

021625	Screwdriver	1	All

017248	Pliers, side cutting	1	All

011188	Pliers, for gudgeon pin circlips	1	All

017246	Gun, grease	1	All

017114	lnflator,tyre	1	All

017052	Spanner, double end,  3/16 in. by 1/4 in	2	All Singles

017052	Spanner, double end, 3/16 in. by 1/in.	1	All Twins

017053	Spanner, double end, 5/16 in. by 3/in.	1	All

017007	Lever, tyre	2	All

018178	Spanner, double end, 1.010 in. by 1.2 in	1	All

017257	Spanner, double end, 3/16 in. by .375 in	1	All

023284	Spanner, for frame stay unit	1	All

017252	Spanner, box, with tommy bar, for sparking plug	1	All

018055	Allen key, for handlebar clip screw	1	All

017249	Wrench, adjustable	1	All

018667	Allen key, for fork crown pinch bolt	1	All

015264	Spanner, 'rocker spindle lock nut	1	All Twins

015213	Spanner, box, 5/16 in	1	All Twins

017254	Spanner, dynamo and clutch	1	All

000174	Washer, brake shoe pad adjustment	8	All

015023	Spanner and gauge, for magneto	1	All Twins

024365	Gauge, feeler, for contact set	1	G3LS,G80S

017482	Holder, valve, for grinding	1	All Singles

011381	Holder, valve, for grinding	1	All Twins

018276	Compressor, for valve spring removal	1	All Singles

022011	Disc timing (see Instruction Book)	1	All

015273	Extractor, for timing pinion and magneto gear	1	All Twins

015374	Extractor, for camshaft gears	1	All Twins

024328	Extractor, bolt for contact breaker	1	G3LS,G80S

018691	Bar locking, for fork crown	1	All

023271	Crash bar, kit complete	1	G3LS,G80S,G9,G11

023226	Bar, only	1	G3LS,G80S,G9,G11

023232	Bolt, top for crash bar	1	G3LS,G80S,G9,G11

023231	Distance piece, crash bar	1	G3LS,G80S,G9,G11

023238	Bracket, bottom assembled, for crash bar	1	G3LS,G80S,G9,G11

023348	Stud, bottom (frame uniting), for crash bar	1	G3LS,G80S,G9,G11

000009	Washer, plain, top fixing bolt	2	G3LS,G80S,G9,G11

000002	Nut, top fixing bolt	1	G3LS,G80S,G9,G11

023466	Panniers, complete set, frames, bags and fittings set	1	G3LS,G80S,G9,G11

022824	Bag, pannier, only, left or right	2	G3LS,G80S,G9,G11

023289	Frame, only, for pannier bag, left	1	G3LS,G80S,G9,G11

023290	Frame, only, for pannier bag, right	1	G3LS,G80S,G9,G11

022827	Bolt, fixing frames, at bottom	2	G3LS,G80S,G9,G11

000347	Bolt, fixing frames, at top	2	G3LS,G80S,G9,G11

000073	Nut, bottom fixing bolt	2	G3LS,G80S,G9,G11

018160	Nut, top fixing bolt	2	G3LS,G80S,G9,G11

000012	Washer, top fixing bolt	2	G3LS,G80S,G9,G11

024402	Panel set	1	G3LS,G80S

024313	Panel, left (off-white)	1	G3LS,G80S

024314	Panel, right (off-white)	1	G3LS,G80S

023360	Bead, for tank panel (red)	2	G3LS,G80S

023371	Screw, for tank motif	4	G3LS,G80S

000070	Bolt, for knee-grip plates	4	G3LS,G80S

000172	Washer, large, for  knee-grip plates	4	G3LS,G80S

000178	Spacer, thin, for knee-grip plates	2	G3LS,G80S

000639	Spacer, thick, for knee-grip plates	2	G3LS,G80S

023291	Set of decarbonising gaskets	1	G3LS,G80S

023170	Set of decarbonising gaskets	1	All Twins

024426	Set of overhaul gaskets	1	G3LS,G80S

024429	Set of overhaul gaskets	1	All Twins